## Slide 2
Motivation & Scope
Can Deep Reinforcement Learning (DRL) be effectively
leveraged for autonomous exploration?
Autonomous exploration is a complex task
Classical analytical methods exist but present some limitations
Learning-based methods can provide more adaptive models
Develop a framework to investigate the possibility of integrating learning-based methods with classical ones
Objective:

## Slide 3
4 / 17
Context: Autonomous Exploration
Exploration: systematically map an unknown environment
Autonomous: the agent can perceive and moves without human guidance
Why autonomous exploration?
Complex task, require simultaneous:
  Mapping
  Localization
  Navigation
  Decision making
Autonomous exploration application examples
The agent must decide where to move next

## Slide 4
4 / 17
Classical Approaches
Next Best View approach Optimization problem, find the next best position for the sensing apparatus
Frontier-Based Exploration (Yamauchi 1997)
  Frontiers: boundary between explored and unknown regions
  Often grouped into cluster
  The agent moves toward frontier clusters
  Fixed heuristics policies to decide which frontier region
Frontier-based exploration illustration

## Slide 5
Deep Reinforcement Learning
Reinforcement Learning
An agent observe and interact with an environment and receives a scalar reward
RL loop: observe state , perform action leading to , receives reward
Goal: learn to take the best action → maximize cumulative reward
A behavioral Policy output an action given a state
A Q-function allow to assign a value to each action-state pair

## Slide 6
Deep Reinforcement Learning
Q Learning
Q-Algorithm allows to iteratively estimate the Q-function from experience
For high dimensional state spaces the Q-table can become excessively memory expansive
In Deep Q-Network the Q-function mapping is approximated by Deep Neural Network
Deep Q-Network
In Q-learning the Q-function is encoded in a table called Q-table

## Slide 7
7 / 17
System Architecture
Hybrid modular architecture
Classic analytical components
Mapping
Frontier detection
Low level navigation
DRL component
Decision making module
Selection of the target position

## Slide 8
The Simulator
Partially observable discrete map
Static maps with random obstacle placement
Agent observes a local window within his perception range
Sequential observations are used to build a believes map
The environment – 2D occupancy grid

## Slide 9
The Simulator
Discriminate frontier cells
Group theme into clusters, splitting them if needed
Compute cluster’s centroids
Frontier detection system
Compute an obstacle free path to the target position (A* algorithm)
Obstacle avoidance path planner

## Slide 10
The Simulator
Configuration setup
Grid size 20x20
Obstacle probability 0.05
Perception range n = 3 cells
Policy: greedy min distance heuristic
Simulation rendering example – Heuristic policy
Simulation rendering

## Slide 11
DRL Module: Observations & Actions
Observation Space (What it sees)
Configurable setup:
Per-cluster frontiers information vector:
  centroids position
  information gain
  distance
Agent position (optional)
Padded to fixed length N for consistent DNN input
Action Space (What it does)
Discrete: select one of N frontier cluster centroids
Chosen centroid passed to Path Planner for navigation
Action (e.g. = 2):
Observations:

## Slide 12
DRL Module: Reward Shaping
Reward Shaping Comparison
Condition | Reward 1 |  |  | Reward 2 | 
Action outcome |  |  |  |  | 
Action selects padding slot | large negative | truncated | truncated | small negative | continues
No new cells explored | small negative | — | — | = R1 | —
Some cells explored | proportional positive | — | — | = R1 | —
Episode termination |  |  |  |  | 
Exploration ≥ threshold | large positive | terminated |  | = R1 | = R1
Max steps exceeded | large negative | truncated |  | = R1 | = R1
No progress for ≥ 20 steps | intermediate negative | truncated |  | = R1 | = R1
Additional signal — Reward 2 only |  |  |  |  | 
Oscillating behavior detected | — |  |  | small negative | 

## Slide 13
Experimental Campaign
Phase 1 — Configuration search: reward × observation set → best configuration per reward
Phase 2 — Hyperparameter optimization: → converged to a single optimal hyperparameter set
Phase 3 — Training budget: 500k / 750k / 1M time steps → 2 best models selected

## Slide 14
Results Metrics & Baselines
Heuristic policy | Mean Reward | Standard dev.
Greedy min distance | 16.48 | 1.78
Greedy max Information gain | 15.01 | 1.12
Heuristic policy | Mean Reward | Standard dev.
Greedy min distance | 16.48 | 
Greedy max Information gain | 15.01 | 
TD loss (training loss)
Mean cumulative episode reward
  Evaluation reward
  Training reward
Mean reward - heuristics baselines

## Slide 15
Results — Model 1: Degenerate Policy
Configuration: Centroids relative positions · Sorted by distance · Reward 1 · 1M steps
Episode reward
TD loss
Evaluation reward | 
Mean | Std. Dev.
16.91 | 0.57
Action distributions |  |  |  | 
Action | 1 | 2 | 3 | …
Probability | 1.0 | 0.0 | 0.0 | 0.0

## Slide 16
13 / 17
Results — Reward Hacking Analysis
Interpretation
The only policy learned always chose action = 0
Diverging huge TD loss
Degenerated Policy
Root cause
Padding always at end + Large penalty → Strong incentive to chose action = 0
Sorted Centroids → Choosing correspond to the greedy heuristic
Not meaningfully learning from observations

## Slide 17
Results — Model 2: Successful Policy
Configuration: Absolute centroids positions · Not-sorted · Agent position · Reward 2 · 1M steps
Evaluation reward | 
Mean | Std. Dev.
15.55 | 2.45
Action distributions |  |  |  |  | 
Action | 1 | 2 | 3 | 4 | …
Probability | 0.51 | 0.25 | 0.21 | 0.028 | 0.00
Episode reward
TD loss

## Slide 18
Results — Model 2: Successful Policy
Good overall performance, comparable with heuristics
Bounded small TD loss
Varied action choice
The model is genuinely learning
Action distributions - sorted by distance |  |  |  |  |  |  | 
Action | 1 | 2 | 3 | 4 | 5 | 6 | 7
Probability | 0.62 | 0.19 | 0.085 | 0.063 | 0.016 | 0.021 | 0.003
The policy learned is
different from the heuristic
Interpretation

## Slide 19
Results — Model 2: Successful Policy
Configuration setup
Grid size 20x20
Obstacle probability 0.05
Perception range n = 3 cells
Policy: trained Model 2
Model 2 simulation rendering
Simulation rendering example – Heuristic policy

## Slide 20
Results — Comparison Summary
Evaluation on 100 test episodes per map size. Metric: mean episode reward at episode end (coverage 90%).
Model | Reward | Obs. Order | 20×20 Coverage | 30×30 Coverage | Outcome
Greedy min distance | — | — | 16.48 1.78 | 36.39 1.27 | Nearest frontier
Greedy max Information gain | — | — | 15.01 1.12 | 34.32 2.58 | Nearest frontier
Model 1 | 1 | Relative - Sorted | 16.91 0.57 | — | ⚠ Degenerate
Model 2 | 2 | Absolute + Agent Unsorted | 15.55 2.45 | 31.46 | ✓ Converged
Model | Reward | Obs. Order | 20×20 Coverage | 30×30 Coverage | Outcome
Greedy min distance | — | — |  |  | Nearest frontier
Greedy max Information gain | — | — |  |  | Nearest frontier
Model 1 | 1 | Relative - Sorted |  | — | ⚠ Degenerate
Model 2 | 2 | Absolute + Agent Unsorted |  |  | ✓ Converged

## Slide 21
Conclusions
A DRL model was successfully integrated in a modular frontier-based exploration pipeline
Reward hacking revealed the critical influence of observation and reward configuration on the learned policy
Model 2 demonstrates convergent training with stable loss — a proof-of-concept for learned frontier selection
The developed framework can be considered validated by the meaningful results obtained
Future work: end-to-end DRL system, multi-agent settings, dynamic and 3D environments, more complex information structures
Paolo Spallanzani · Università degli Studi di Modena e Reggio Emilia · A.A. 2024/2025